## Slide 1: 1.6-1
Wellbore Hydraulics,
Pressure Drop Calculations

## Slide 2: 1.6-2 Wellbore Hydraulics
Hydrostatics
Buoyancy
Pipe Tension vs. Depth
Effect of Mud Pressure
Laminar and Turbulent Flow
Pressure Drop Calculations
  Bingham Plastic Model
  API Power-Law Model

## Slide 3: 1.6-3 Buoyancy Force = weight of fluid displaced (Archimedes, 250 BC)
Figure 4-9. Hydraulic forces acting on a submerged body

## Slide 4: 1.6-4 Effective (buoyed) Weight
Buoyancy Factor
Valid for a solid body or an open-ended pipe!
We = buoyed weight
W = weight in air
Fb = buoyancy force
V = volume of body
f = fluid density
s = body density

## Slide 5: 1.6-5 Axial Forces in Drillstring
Fb = bit weight
F1 & F1 are pressure forces

## Slide 6: 1.6-6 Axial Tension in Drill String
Example
A drill string consists of
10,000 ft of 19.5 #/ft drillpipe and
600 ft of 147 #/ft drill collars
suspended off bottom in 15#/gal mud
(Fb = bit weight = 0).
What is the axial tension in the drillstring as a function of depth?

## Slide 7: 1.6-7 Example
Pressure at top of collars
= 0.052 (15) 10,000 = 7,800 psi
Pressure at bottom of collars
= 0.052 (15) 10,600 = 8,268 psi
Cross-sectional area of pipe,
A1
10,000’
10,600’

## Slide 8
Cross-sectional area of collars,
A2
A1
1.6-8 Example – cont’d

## Slide 9: 1.6-9 Example - cont’d
1. At 10,600 ft. (bottom of drill collars)
Compressive force = p A
= 357,200 lbf
[ axial tension = - 357,200 lbf ]
4
3
2
1

## Slide 10: 1.6-10 Example - cont’d
2. At 10,000 ft+ (top of collars)
FT = W2 - F2 - Fb
= 147 lbm/ft * 600 ft - 357,200
= 88,200 - 357,200
= -269,000 lbf
4
3
2
1
Fb = FBIT = 0

## Slide 11: 1.6-11 Example - cont’d
3. At 10,000 ft - (bottom of drillpipe)
FT = W1+W2+F1-F2-Fb
= 88,200 + 7800 lbf/in2 * 37.5in2 - 357,200
= 88,200 + 292,500 - 357,200
= + 23,500 lbf
4
3
2
1

## Slide 12: 1.6-12 Example - cont’d
4. At Surface
FT = W1 + W2 + F1 - F2 - Fb
= 19.5 * 10,000 + 88,200 + 292,500 - 357,200 - 0
= 218,500 lbf
Alternatively: FT = WAIR * BF
= 283,200 * 0.7710 = 218,345 lbf
4
3
2
1

## Slide 13: 1.6-13
Fig. 4-11. Axial tensions as a function of depth for Example 4.9

## Slide 14: 1.6-14 Axial Load with FBIT = 68,000 lbf